## Slide 1: Water based process for Delaminating and Deinking surface printed plastic

## Slide 2
8.3 billion tonnes of plastic produced since 1950
Almost 80% landfilled, incinerated or leaked into the ocean
90,5% of total plastic production has never been recycled
There is not a real recycling. Recycled plastic goes to low-added value applications
It is a “cradle to grave” economy

## Slide 3
THE PROBLEM
Multilayer plastic packaging is not recyclable
40 billion multi-material packages per year (US only)
Approximately 20% of total flexible packaging production
 more than 9,6 tonnes of multilayer plastic
1
Image obtained from: https://www.materialsrecoveryforthefuture.com/research-results/seeding2-2/
Each layer requires different temperatures to be recycled

## Slide 4
Inked recycled plastic goes directly to downcycling
2
30% of flexible packaging is surface printed
Inks/adhesives cannot be removed, recycled plastic can be used only for low added value products
THE PROBLEM
Printed ink spoils the recycled product both visually and in its mechanical properties

## Slide 5
10% Industrial production never ends in the market
3
Failures in the manufacturing process cause 8,8 M tonnes of multilayer and inked plastic that go directly to landfilling before entering in the market
THE PROBLEM

## Slide 6
Cadel Deinking has developed an innovative technology able to separate multi-material flexible packaging into its constituent materials (PE / PET). This technology can also remove printed ink from plastic surfaces before they are recycled, obtaining a high value product again.
This technology is a chemical and mechanical recycling process that creates viable material feedstocks for new manufacturing processes from multi-material flexible packaging. Cleaning chemicals with water-based formulations are used in the process; neither solvents nor environmentally hazardous chemicals are used.
THE SOLUTION

## Slide 7
LABORATORY RESULTS
Polymer A + Polymer B
Polymer A
(PET + ink)
Polymer B
(PE + adhesive)
DELAMINATING
DELAMINATING + DEINKING
Polymer A + Polymer B
Polymer A
(PET deinked)
Polymer B
(PE without adhesive)
THE SOLUTION

## Slide 8
DELAMINATING TECHNOLOGY - APPLICATIONS
THE SOLUTION
Laminated PET//PE
Metallized BOPP//BOPP

## Slide 9
DEINKING TECHNOLOGY - APPLICATIONS
THE SOLUTION
LDPE FILM
RIGID HDPE
PP
BOPP LABEL

## Slide 10
DELAMINATING & DEINKING TECHNOLOGY- THE PROCESS
THE SOLUTION

## Slide 11
DELAMINATING & DEINKING TECHNOLOGY- THE PROCESS
CLOSED LOOP
Solvent
Free
TRL 9: Proved in operational environment
TRL 4: Validated laboratory tests
THE SOLUTION
Extended to more than 20 countries

## Slide 12
DELAMINATING & DEINKING TECHNOLOGY- THE PROCESS
Grinding: Operation executed at the beginning, when the plastic enters the system.
Delaminating: Innovative technology to separate the plastic materials in laminated inked packaging film. It is necessary to use different temperatures and additive concentration for each material (PE-PET) during the process.
Deinking: The milled material goes to the reactors, where it is in contact with a solution based on water-based deinking reagents that removes the ink from the surface of the plastic. After the first wash, the ink emerges from the plastic surface and remains in the aqueous solution.
Rinsing: The plastic is centrifuged and rinsed with fresh water to achieve the final quality of the ink-free and process chemicals-free plastic.
Drying: The plastic material goes to a new centrifugation step to eliminate any residual moisture.
Regranulating: Once the plastic is dried, it is sent to the extrusion step where the ink-free pellets are generated.
Sorting: A previous process of classification is necessary to separate the different plastic materials.
THE SOLUTION

## Slide 13
THE SOLUTION
PILOT PLANT
CADEL DEINKING owns a pilot plant in Sant Vicent del Raspeig (Alicante) that can process the material, following all the steps of industrial production.
https://youtu.be/O793xr7F00s
Delaminating
NEW
SCALABLE TECHNOLOGY
The next step is to scale the delaminating process  Optimization (time/solvent concentration)

## Slide 14
BUSINESS OPPORTUNITY
TARGET CUSTOMERS
https://www.planettogether.com/blog/scheduling-in-the-flexible-packaging-industry
https://www.herbold.com/es/erfolgsgeschichte-im-recycling-fuer-post-consumer-und-folienabfaelle-mit-rodepa-plastics-b-v-und-herbold-meckesheim-gmbh/
CONVERTERS
RECYCLERS
Close to 13,000 companies
45MT of plastic production
2,000T of plastic waste
€280 billion turnover
Close to 5,000 companies
1,000T of plastic production
€10 billion turnover

## Slide 15
POTENTIAL MARKET
BUSINESS OPPORTUNITY
Multilayer
20% of total plastic production
69.9MT
348,000,000 tonnes of plastic produced worldwide in 2017
Inks and adhesives
30% of flexible plastic packaging
18.8 MT
Industrial waste
10% of plastic manutacturing
6.9MT
1.8 MT
Potential market
97.4 MT
Notes: PLASTIC PRODUCTION WORLDWIDE: 348MT (2017)
FLEXIBLE PLASTIC PACKAGING  18% 
MULTILAYER  20%
INKED

## Slide 16
BUSINESS OPPORTUNITY
ECONOMIC ADVANTAGES OF D&D TECHNOLOGY
VIRGIN PELLETS COST  €1,200/T
D&D RECYCLED PELLETS COST  €700/T
SAVINGS OF
€500/T
Printed and laminated plastic waste
€350/T
Delaminating and Deinking
€200/T
Regranulating
€150/T
D&D Recycled pellets
€700/T
Delaminating process is at laboratory scale. Costs could be slightly higher
Decreased carbon footprint 5 times
595 kgCO2/t plastic

## Slide 17
BUSINESS OPPORTUNITY
BUSINESS MODEL
DIRECT SALES
LICENSE AGREEMENTS
TURNKEY PROJECTS
Complete D&D industrial plant
500-1,000kg/h capacity
Engineering & Equipment supply/installation
CHEMICAL REAGENTS
Own designed combination of chemicals for delaminating and deinking
Manufactured and distributed by CADEL
TECHNICAL ASSISTANCE
ADDITIONAL SERVICES
Technical assistance (SAT) per remote access
24/7 on-line support
Expert advice on operation and maintenance
Additional technology improvements in new hardware
Implemented at customer’s plant
€1.3M (converters)
€1.7M (recyclers)
€180k/year per plant
€50/year
€50/year

## Slide 18
BUSINESS OPPORTUNITY
BUSINESS MODEL
Chart: 
| 2019.0 | 2020.0 | 2021.0 | 2022.0
Turnkey plants | 2 | 3 | 5 | 8
Licence agreements | 4 | 8 | 13 | 20
POTENTIAL BUSINESS
SALES EVOLUTION
Chart: 
| 2015.0 | 2016.0 | 2017.0 | 2018.0 | 2019.0 | 2020.0
Sales | 19000 | 288000 | 500000 | 2600000 | 5540000 | 6970000

## Slide 19
BUSINESS OPPORTUNITY
MARKET FEASIBILITY
200 companies have shown interest in our delaminating and deinking technology
41 Have sent material
31 Industrial tests paid
11 Film tests & validation
FIRST PLANT SOLD!
9 Customers in
advanced negotiations

## Slide 20
OUR COMPANY
Start of activity
Launch into market
Market positioning
Foundation
2010
2014
2015
2017
CADEL DEINKING is a technological and innovative engineering company located in Alicante, Spain
Since the beginning, CADEL has been developing innovative, environmentally friendly and low-cost processes to recycle and reuse plastic waste
The objective is to improve the quality of the plastic products through the most sustainable method
PRESENTATION

## Slide 21
OUR COMPANY
TEAM
CADEL is fundamentally a R&D Company, based on a multidisciplinary, dynamic and motivated human team
R&D
Technical office
Process
Engineering
Automation
and
Control
Electrical
engineering
Documents
2 Business & Financial Managers
2 PhDs in Chemical Engineering
4 Chemical Engineers
4 Electrical & Automation Engineers
2 Industrial Engineers
1 Industrial Design Engineer
1 Electrical Assistant
1 Sales & Marketing Assistant

## Slide 22
OUR COMPANY
CADEL OPEN DAYS
Last 4th, 5th and 6th December, we celebrated the first Open Days for Delaminating and Deinking technology at CADEL DEINKING facilities. During this event, we demonstrated the operation of a plant, which allowed the visitors to understand the D&D process.
More than 62 companies from 26 different countries around the world attended, showing their interest in the plant. Also high-level speakers showed their vision on circular economy.

## Slide 23
CADEL OPEN DAYS
OUR COMPANY

## Slide 24
OUR COMPANY
CADEL OPEN DAYS

## Slide 25
OUR COMPANY
CADEL OPEN DAYS

## Slide 26
OUR COMPANY
CADEL OPEN DAYS

## Slide 27
OUR COMPANY
CADEL OPEN DAYS

## Slide 28
OUR COMPANY
CADEL OPEN DAYS

## Slide 29
OUR COMPANY
CADEL OPEN DAYS
Karlheinz Hausmann from Dow DuPont
Andreas Dirnberger from EREMA

## Slide 30: THANKS FOR YOUR ATTENTION